## Slide 1: IoT Bluemix Tutorial
Christian Decker, HHZ, Reutlingen University
Sebastian Mantsch, MHP

## Slide 2: Rapid IoT Application Development
… in the past
Source: Werbefarbik, blickpixel, pixabay.com

## Slide 3: Rapid IoT Application Development
It felt like …
Source: WikiImages, pixabay.com

## Slide 4: Rapid IoT Application Development
COTS technology, e.g. mobile phones with increasing number of sensors
Today…
Source: Geisse et al., A survey on smartphone features relevant for reality mining. Digital Enterprise Computing (DEC 2016) P-258, 107-116 (2016)

## Slide 5: Rapid IoT Application Development
Powerful cloud-based backend systems
Today…
Source: OpenClipart-Vectors, pixabay.com

## Slide 6: This Tutorial
… will facilitate IoT research using standard sensor technology and a powerful backend.
COTS sensor technology
Cloud-based IoT Platform
+

## Slide 7: Agenda
Preparations
IoT Platforms
MQTT
Bluemix Introduction
Example Applications

## Slide 8: Material
Hosted on Github repository
https://bit.ly/iotbluemix

## Slide 9: Before we start…
Get your trial account
Go to github repository
https://bit.ly/iotbluemix
Deploy example apps in Bluemix
  Phone Sensor Repository
  NodeRED Repository
Enter account credentials when required

## Slide 10: IoT Platforms
General Architecture

## Slide 11: Everybody has one…They are everywhere
Amazon, Microsoft, IBM, Oracle, …
It is estimated, that there are 100+ platforms out there.
Lists are always incomplete…
Source: http://internetofthingswiki.com/top-10-iot-platforms/634/

## Slide 12: IoT Platforms – Core Functions
Device Management
  Device connection and integration, infrastructure operations
  Devices become abstract things; accessible for other systems
Business Rules
  Management and operation of business logic for event handling
Process Engine
  Defines logical process steps of an application
Data Service Integration
  Integration of external services for IoT application, e.g. REST based web services

## Slide 13: How do IoT Platforms work?
They run in a cloud environment.
They virtualize a real-world IoT environment.

## Slide 14: IoT Service and Virtual Entity Abstraction
Physical World
IoT Service
Level
sensor
sensor
actuator
sensor
sensor
Virtual entity-based model models relevant
aspects of Physical World
Virtual Entity
Level
IoT System
Resources exposed as IoT Services measure,
observe and
actuate on
Physical World
Association of IoT Services
to modelled Virtual Entities
Give me the
indoor
temperature in
Room 1.23
Example Interactions
Give me the
value of Temperature
Sensor 456
Set Actuator 867
To “on”
Set light level
In Room 2.57
to 15
Source: EU FP7 Projekt „IoT-A: Internet of Things Architecture“, Slides by Carsten Magerkurth (SAP), April 2013

## Slide 15: IoT Platforms
Cloud-based middleware betw. IoT devices and applications
Virtualize the real world by realizing an entity abstractions.
Core functions
Device management
Business Rules
Process Engine
Data Service Integration
Other functions
Analytics, Big Data Processing
Credentials, tenant management
UI Designer, Mashup Builder
Purpose
Design, build and execute IoT applications
Designer / Composer / IDE for application designs, partially codeless
Take away
Source: jp26jp, pixabay.com

## Slide 16: Connecting Devices using MQTT

## Slide 17: MQTT Message Queue Telemetry Transport
Said to be THE IoT protocol
Lightweight messaging protocol on top of TCP/IP
Interesting features
Pub / Sub communication model
Implemtations for all kind of (embedded) devices and lots of programming languages available
Supported by basically every IoT plattform

## Slide 18: Pub / Sub Communication
Source: http://www.hivemq.com/blog/mqtt-essentials-part2-publish-subscribe

## Slide 19: Topic Specification and Filtering
A topic specifies a message queue
A client subscribed to a topic receives all messages from this queue
Source: http://www.hivemq.com/blog/mqtt-essentials-part-5-mqtt-topics-best-practices

## Slide 20: Topic Specification and Filtering
Single level specification will match to all messages from …
Source: http://www.hivemq.com/blog/mqtt-essentials-part-5-mqtt-topics-best-practices

## Slide 21: Topic Specification and Filtering
Multi-level specification will match all messages from …
Source: http://www.hivemq.com/blog/mqtt-essentials-part-5-mqtt-topics-best-practices

## Slide 22: Bluemix Intro

## Slide 23
IoTBluemixTutorialNode
IoTBluemixTutorialPhone
Services
iot-cloudant-cloudantNoSQLDB
iot-iotf-service
Dashboard
Multiple instances of a cloud foundry application
Different applications may point to same services
Application Landscape

## Slide 24: Bluemix MQTT Topic Specification
Always starts with iot-2
iot-2/type/<type-id>/id/<device-id>/evt/ <event-id>/fmt/<format-id>
Example
iot-2/type/iotphone/id/ testDevice/evt/sensorData/fmt/json
MQTT sample data payload
any
any

## Slide 25: Node-RED
Node-RED is a node.js based tool for wiring together hardware devices, APIs and online services in new and interesting ways.
Node-RED home: https://nodered.org
Bluemix utilizes Node-RED as rapid development tool

## Slide 26: Example Applications

## Slide 27: Login
Use URL to login in EU / UK Zone
https://console.eu-gb.bluemix.net/

## Slide 28: Bluemix Phone App Acquire Data and Display
Access URL and choose device ID
Login into Bluemix, copy URL (w/o https), …
Sensor data
Using MQTT over websockets

## Slide 29: Device Centric Analytics Working with Data

## Slide 30: Rule Centric Analytics Alerts using Data

## Slide 31: Node-RED App
Bluemix uses Node-RED as visual composer for rapid application development
More possibilities to work, analyze, store IoT data
Connect with external (REST based) data services, e.g. Twitter

## Slide 32: Access Node-RED App from Dashboard

## Slide 33: Launch Node-RED App